## Slide 1: Performance
David Monismith
Jan. 16, 2015
Based on notes from Dr. Bill Siever and from the Patterson and Hennessy Text

## Slide 2: Outline
Last time
  Finished history and a beginning on performance evaluation.
This time
  Continued Performance evaluation

## Slide 3: Recall
Performance = how good is it? But need to know what to measure and how to measure it.
Discussed Speed, Operations per second, Efficiency (e.g. Power)
Other measures include bandwidth, latency, and cost
  Bandwidth - How much data can be transmitted over a line per unit time
  Latency (Memory, Disk) - How long does it take to retrieve data (e.g. disk access time)
  Resource Cost - $/GB, $/unit, $/GHz

## Slide 4: Recall
Performance = 1/execution time
Speedup = performance_of_computer_1/performance_of_computer_2

## Slide 5: Dividing Up Execution Time
Execution time can be divided into two parts
The whole is called user time or wall time
  This is the time the user spends waiting for the program to finish.
  The time the program actually runs is CPU time
  The time used for the system services (OS, IO, waits, etc.) is called System CPU time
Try running top on a Linux or Mac machine at the terminal to see how much CPU time is used in running programs
For this class we will only be concerned with user time as we will assume System CPU time is small enough to be negligible

## Slide 6: Clock Time
Hz - Hertz = cycles per second
MHz - 1000000 Hz, GHz - 1 billion Hz
A Clock signal can be thought of as a square wave (an on/off pulse)
  The CPU clock governs how quickly data passes through CPU
  Data is part of assembly instructions
  Instruction delegates the data path

## Slide 7: Clock Time
The Clock signal delays data from moving from component to component in CPU (i.e. register to ALU/CU, ALU to CU, data to memory, data from memory)
Recall from math, waveforms have a period and frequency
  frequency = clock_speed
  period = 1/frequency (i.e. seconds per cycle)
For a 1MHz processor frequency, period is 1 microsecond (1e-6)
For a 1GHz processor frequency, period is 1 nanosecond (1e-9)
What is the period for a 250MHz processor (4 ns)? 500MHz (2 ns)?

## Slide 8: Clock Waveforms
+-------+
| |
| |
| |
--------+ +------- . . .
High in the waveform above represents on and low represents off.
Note that the wave form above could use zero/off to represent time in doing work in a CPU component and one/on to represent transition time.
Transition time and computation time are not necessarily equivalent.

## Slide 9: Instructions
Instructions can be very different from machine to machine
  RISC vs. CISC machines
Some processors use same # of cycles per instr
Others have differing instruction counts
Simple computation for time CPU performs processing
CPU Time = total CPU cycles * cycle time

## Slide 10
Analytical performance calculations may answer one of a few questions:
How long will a program run?
What happens if we improve performance/want a certain performance?
(e.g. what if we want a program to run in 1.0s)
How can we make two machines that require a different number of cycles per
instruction (CPI) to run a program in the same amount of time?

## Slide 11
Data for such problems may include:
A list of instructions and cycles required by each
A clock speed or period
Average CPI (Clocks/Instruction) for a specific program
Sample code with a CPI table
Answer might require run time, instruction count, etc.

## Slide 12: Run Time
What is the run time of a program requiring 1,250,000 cycles on a 50MHz machine?
1 cycle = 1/50,000,000 = 20ns
20ns*1,250,000 = 0.025s

## Slide 13: CPI Equation
Execution time = # of instructions * cycles/instruction * time/cycle
This is tool for understanding tradeoffs in the design of instruction sets, processor pipelines, and memory system organizations.

## Slide 14: Cycles Per Instruction Example
Given a program with an average CPI of 2.5 for 20,000 instructions that runs on a processor with a 10ns clock, find the clock frequency and program runtime.

## Slide 15: Solution
Frequency = 1/1e-8s --> 1e8 Hz --> 100 MHz
Total cycles = 2.5 cycles/instr * 20,000 instr = 50,000 cycles
Run time = 50,000 cycles * 10ns/cycle = 500,000ns = 0.5ms

## Slide 16: Finding the Runtime Example
Given a program with 1,000,000 instructions costing 6 cycles each and 2,000,000 instructions costing 3 clocks cycles each, find the frequency needed to complete the program in 1s and 0.5s.

## Slide 17: Solution
6*1,000,000+3*2,000,000 = 12,000,000 cycles
To complete in 1s, divide by 1s to get 12,000,000 cycles/s = 12 MHz
To complete in 0.5s, divide by 0.5s to get 24,000,000 cycles/s = 24 MHz