## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and from the Patterson and Hennessy Text

## Slide 2: Last Time
Review of analytical performance measures
Clock speed (frequency = cycles per second)
Clock wave, period = 1/frequency
Clock allows for CPU components to do work and transfer data to the next location in the data path
Review of cycles per instruction
CPI*#instructions*clock time (period) = run time
Reviewed Examples

## Slide 3: Class Poll
Does a chip with a higher clock frequency than another chip always result in a faster runtime?

## Slide 4: Instruction Set Architecture
Instruction Set Architecture (ISA) - ability of a processor to utilize a specific set of 1's and 0's as an operation
Intel and AMD processors of the same age likely use the same ISA.
Chips with the same ISA should be able to read and run the same executable program.

## Slide 5: Operations, Opcodes, and Operands
Operations such as ADD, SUB, JUMP, etc consist of an opcode and operands
Opcode - binary representation of the operation (ADD, SUB, JUMP, etc.)
Operands - registers or memory locations of data ($r1, $r2, …)

## Slide 6
Different ISA implementations may use different opcodes.
For example, 0x77 may mean ADD on one ISA and JUMP on another.
Implementation or how the processor runs a program may vary.

## Slide 7: Example
Clock speed and cycles per instruction both impact performance
  Intel 1.8 GHz Machine with 4 CPI for ADD
  AMD 1.5 GHz Machine with 3 CPI for ADD
Which is faster? AMD, in this case
Why?
  1.5GHz / 3 CPI -> 5*10^8 instr/s for AMD ADD
  1.8GHz / 4 CPI -> 4.5*10^8 instr/s for Intel ADD
Assuming the same ISA, the AMD machine is 11% faster for ADD.
Often Intel and AMD processors have different pipeline implementations and clock speed is not good as a sole indicator of performance.

## Slide 8: Amdahl’s Law
Gene Amdahl - discovered maximum theoretical speedup when parallelizing a sequential program, worked with and developed mainframe computers during the 1950's and 60's, and created several mainframe and supercomputing corporations from the 60's – present.
Amdahl's Law - a program can only run as fast as its slowest part.
For speedup of a sequential program using parallelism, such a program can only improve to the runtime of the part that cannot be parallelized.
This is equivalent to the law of diminishing returns.
Effectively, this means you can't go any faster than your slowest part.
The sequential portion will dictate the highest possible speed in both Hardware and Software

## Slide 9: Example
New_Execution_Time = Parallelizable_Execution_Time/Parallel_Factor + Sequential_Execution_Time
Assume a program with a 90s run time on a sequential processor where 80s is parallelizable. 10s is the fastest the program could ever run.
10s = 80s/infinity + 10s
If we use a dual core processor the run time is 50s = 80s/2 + 10s
If we use a quad core processor the run time is 30s = 80s/4 + 10s
If we use an 8 core processor the run time is 20s = 80s/8 + 10s

## Slide 10: Computing Speedup
The speedup using a quad (4) core processor vs. a sequential processor is 90s (seq. runtime) / 30s (quad core runtime) = 3
The maximum theoretical speedup is 90s (seq. runtime) / 10s (infinite parallelism) = 9
Based on Amdahl's law we should make the most commonly used code (i.e. loops) parallel if possible.

## Slide 11: Benchmarking (Experimental Performance Evaluation)
Benchmarks measure performance by using real or model programs to test performance.
Synthetic benchmarks use programs written only to test performance.
Non-synthetic benchmarks use production ("real") programs to test performance.
Synthetic benchmarks can test specific hardware features and should be used early in hardware design.
They are easily fooled though, we can change a processor or compiler and get drastically different performance (e.g. we might have a hardware operation to compute e^x).
Results are often reported in MIPS or FLOPS.

## Slide 12: MIPS and FLOPS on Different Architectures
MIPS - millions of instructions per second
FLOPS - floating point operations per second
These aren't the same on different ISAs though.
RISC - reduced instruction set computing
CISC - complex instruction set computing
RISC machines may need hundreds of instructions to perform a memory fetch.
CISC machines may only need one instruction to do the same.
Thus a RISC machine will show a much higher MIPS rating, but may have the same execution time on the same program as an equivalent CISC machine