## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: Last Time
Instruction Set Architecture
Analytical Calculations
Amdahl’s Law
Average CPI

## Slide 3: This Time
Benchmarking - Experimental Performance Measures.
Synthetic - artificial or a program written only to measure performance.
Non-synthetic - testing with production code ("real" program).
Synthetic benchmarks can test specific hardware features.
They can be easily fooled, though.
If a hardware workaround is discovered, it can beat a synthetic benchmark easily:
  e.g. HW cosine vs. SW cosine.

## Slide 4: Synthetic Benchmarks
Whetstone(floating-point)/Dhrystone(integer) benchmarks are synthetic.
Results often reported in FLOPS (Floating point operations per second) or MIPS (Millions of instructions per second).
Sometimes result are reported in Peak MIPS/FLOPS (using the fastest instruction).
This is useful only when comparing equivalent ISAs as work may differ based upon instruction set.

## Slide 5: Synthetic Benchmarks
RISC - Reduced instruction set computing (e.g. MIPS architecture) could require many (hundreds) of instructions to perform an operation like a memory copy.
CISC - Complex instruction set computing (e.g. Intel or AMD) might require only one instruction to perform the same copy.
Take home message: MIPS rating for RISC will be much higher than CISC.
Execution time of a program gives a better answer

## Slide 6: Non-synthetic Benchmarks
Non-synthetic gives a measure of performance seen by the end-user with real programs.
A common example is SPEC 2006, though there are many others such as FPS for a particular game, file compression speeds, image processing speeds with photoshop, etc.
SPEC 2006 measures int/float performance using some general computer tasks.
Tasks are compute bound (don't rely on I/O much)

## Slide 7: Example SPEC Applications
Integer
  gzip - file compression
  gcc - C compiler
  Chess
  numerical optimization
  database queries
  logical operations
Floating point
  Image Processing/Neural networks
  CFD (Computational Fluid Dynamics
  3D Graphics
  Nuclear Physics
  etc.

## Slide 8: More on SPEC
SPEC is industry driven (HP, Intel, Oracle, IBM, SGI, others).
Warning: results are highly dependent upon compilers.
Good compilers can optimize code for particular architectures.
Intel has their own compilers, and so do other companies (e.g. Portland Group, Cray, Microsoft, etc.).
Warning: I/O takes a significant amount of time in many programs.
Don't assume a benchmark takes this into account.

## Slide 9: Compilation
Compiling to an executable is not the same as Java compilation.
C, C++, Objective C and some other languages are compiled to executable files.
Often such files only work on one architecture.

## Slide 10: Compilation
The compilation process works in the following order:
Source Code -> Compiler -> Assembly Code -> Assembler -> Object file (machine language) -> Linker -> Executable File -> Loader/Operating System -> Execution

## Slide 11: Assembly
Compiler - converts a high level languages into assembly instructions the machine understands.
Assembly is often native to the processor.
Assembly Language is a symbolic representation of the operations a computer understands.
It is a representation of machine language (1's and zero's) that can be read by people, but it may be very difficult to understand.
Assembler - converts assembly language to machine language, filling in details such as addresses and producing object files.

## Slide 12: Linking
Object file - machine language representation of source code.
Linker - tool that binds or links separate object files and completes any missing details.
This tool outputs a file in executable format for the native operating system.
That is, the file may be loaded into memory and executed.
Programs may be self contained (statically linked) or require outside functions/methods (dynamically linked) such as DLLs (dynamically linked libraries).

## Slide 13: Assembly Programs
Pros:
  Consist of short instructions.
  If written properly, smaller and faster than high level language.
  May better use a processor.
  May be necessary for new processors if a compiler isn't yet available.
  May help to debug a program from a high level language.
  May help with benchmarking.

## Slide 14: Assembly Programs
Cons:
  Not portable.
  Tedious to use (many instructions to do simple operations, few variables).
  Very difficult to read.

## Slide 15: Assembly Programming
Format
  Instructions are short and often in format
  INSTR_NAME FIRST_ARGUMENT, SECOND_ARGUMENT, . . .
Data comes in three basic forms
  Registers
  Constants
  Data stored in memory

## Slide 16: Assembly Programming
Instruction types
  Data movement - moving in and out of memory.
  Control - select, call, and loop.
  Data manipulation - mathematical and logical operations.
  Most MIPS instructions play only one role (similar to RISC system).

## Slide 17: Assembly programming
Data
  Stored in binary format.
  Basic data unit for a processor is called a word.
  MIPS word size = Integer register size = 32 bits = 4 bytes.
  No typing for most data - just represented as integers, including bytes, characters, boolean variables, and integers.
  In MIPS, floating point variables are stored in a coprocessor.
  Floats are stored in 32 bit registers and doubles are stored in pairs of 32 bit registers

## Slide 18: Registers
Registers - data storage on the processor
The register file (group of registers on a processor) is similar to an array
The MARS MIPS processor has a register file consisting of 32 integer registers each of which is 32 bits wide.
25 of these registers are available for you to work with, for now.

## Slide 19: Registers
Registers have both numeric and symbolic names
$0 $zero - special register for constant zero
$1 $at - assembler temporary
$2 - $3 $v0 - $v1 - values for function returns and expression evaluation
$4 - $7 $a0 - $a3 - arguments for functions
$8 - $15 $t0 - $t7 - temporary registers
$16 - $23 $s0 - $s7 - saved registers
$24 - $25 $t8 - $t9 - more temporary registers

## Slide 20: In-Class Exercise
Download the MARS MIPS Simulator.
Assemble and run the “Hello, world” example on the class website.
Make note of the different parts of the program including the .data and .text sections.
  Data, including strings and statically allocated arrays are declared in the .data section
  Functions (similar to methods) including main are declared in the .text section
Comments start with a hash symbol (#).
Execution begins at the main: tag.
Read about the li (load immediate), la (load address), and syscall instructions using the MARS help utility.