## Slide 1: Computer Organization – Memory Access
David Monismith
Jan. 30, 2015
Based upon notes by Dr. Bill Siever and the Patterson and Hennessy Text

## Slide 2: Last Time
Review of Load operations
Review of Hex Numbers

## Slide 3: Hexadecimal Numbers
Recall that memory is addressed in binary (32 or 64-bit)
If we use base 16 or hexadecimal numbers, these values can be represented in a more compact manner.
1000 -> 8
1001 -> 9
1010 -> A (10 decimal)
1011 -> B (11 decimal)
1100 -> C (12 decimal)
1101 -> D (13 decimal)
1110 -> E (14 decimal)
1111 -> F (15 decimal)
0000 -> 0
0001 -> 1
0010 -> 2
0011 -> 3
0100 -> 4
0101 -> 5
0110 -> 6
0111 -> 7

## Slide 4: Data Storage In Arrays
Recall that one of the reasons we need to look at binary and hex values is so we can understand how data is stored in memory.
In particular we will look at arrays.
Arrays are stored contiguously in memory. This means each data element is placed one right after the other.

## Slide 5: An Analysis of Arrays
In C and Java, we generally index into arrays without regard for the size of a data element.
For example, given the following Java or C style arrays:
int [] iArr = new int[10] or int iArr[10];
char [] cArr = new char[10]; or char cArr[10];
we access cArr[2] or iArr[5] in the same manner regardless of how the data is stored.
We can do the same with objects.

## Slide 6: Arrays
We access cArr[2] or iArr[5] in the same manner regardless of how the data is stored. We can do the same with objects.
cArr[2] means give me the data at memory address cArr + 2
iArr[5] means give me the data at memory address iArr + 5*4, assuming a 32-bit system
Assume the array name is a label that refers to an offset in memory.
Assuming memory is an array, we are saying memory[label + array index].
cArr[2] means give me the data at memory address cArr + 2
iArr[5] means give me the data at memory address iArr + 5*4, assuming 32-bit integers.

## Slide 7: An Example in C
Given the following example:
int arr[10];
for(i = 0; i < 10; i++) {
arr[i] = 1+i;
printf("arr[%d] is %d\n",
i,arr[i]);
}

## Slide 8: A Similar Example in C
int arr[10];
for(i = 0; i < 10; i++) {
*(arr+i) = 1+i;
printf("arr[%d] is %d\n",
i,*(arr+i));
}

## Slide 9: Converting to Assembly – Declaring a statically allocated array
Declaration and initialization to zero of an integer array is performed in the .data section of an assembly program
Syntax:
  Label: .word 0:arraySize
Example:
  intArr: .word 0:10

## Slide 10: Converting to Assembly
Assume the array name is a label that refers to an offset in memory.
Assuming memory is an array, we are saying Memory[label + array index].
Let's assume for now the label is stored in a register like $s1
We tell the assembler we are referring to data in a memory address as follows:
0($s1)

## Slide 11: Array Offsets in Assembly
We tell the assembler we want to access an offset into memory by changing the value in front of $s1
offset($s1) - Note: offset is a 16 bit signed integer
Example: 4($s1) - 4 bytes past the memory address stored in $s1
8($s1) - 8 bytes past the memory address stored in $s1
Data at a memory address must be loaded before it may be used.

## Slide 12: Loading Array Data
When using 32-bit data units (words), the lw or load word instruction is used to load data from memory into a register.
Syntax:
lw destination_register, source_address
Example
lw $s2, 0($s1) #load the data at memory
#address $s1 into $s2
lw $s2, 4($s1) #load the data at memory
#address $s1 + 4 into $s2

## Slide 13: Issues with Low Level Memory
Warning: Memory is stored differently on different processors!
Memory has an endianness, referring to the order in which the bits in memory are stored for each byte/word.
Big endian - first byte in a word is the most significant bits, last byte is the least significant bits.
Little endian - first byte in a word is the least significant bits, last byte is the most significant bits.
MIPS is a Big Endian Machine.

## Slide 14: Example
Assume we have some memory allocated (an array)
Mem[0] = 0x00
Mem[1] = 0x03
Mem[2] = 0x00
Mem[3] = 0x01
Mem[4] = 0x00
Mem[5] = 0x00
Mem[6] = 0x1B
Mem[7] = 0x07
Mem[8] = 0x00
Mem[9] = 0x01
Mem[10] = 0x01
Mem[11] = 0x01

## Slide 15: Example Continued
What if If register s1 contains 0:
  lw $s2,0($s1) -> s2=0x00030001 (decimal 196,608)
  lw $s3,8($s1) -> s3=0x00010101 (decimal 65,793)
What if register s1 contains 4:
  lw $s2,0($s1) -> s2=0x00001B07 (decimal (27*256) + 7 = 6919)
  lw $s3,4($s1) -> s3=0x00010101
  lw $s4, -4($s1) -> s4=0x00030001
What if this was a Little Endian Machine and s1 contains 0?
  lw $s2,0($s1) -> s2=0x01000300
  lw $s3,4($s1) -> s3=0x071B0000
  lw $s4,8($s1) -> s4=0x01010100
What are the decimal values for these?

## Slide 16: Load Word
lw is a "move" command.
It moves data out of memory and into registers.
Notice that integer/32-bit arrays are indexed by segments of four bytes.
We can easily move through such an array.
Assume the address of our array is in $s1 and we wish to get to index 5
  li $t1, 5 # load 5 into $t1
  add $t1, $t1, $t1 # now $t1 is 10 (it's doubled)
  add $t1, $t1, $t1 # now $t1 is 20 (it's doubled # again)
  add $t1, $s1, $t1 # now $t1 contains the address of # index 5 of our array
  lw $t2, 0($t1) #load the value at array[5] into $t2

## Slide 17: Store Word
Another "move" command is sw.
sw moves data out of a register into memory.
sw = store word
Syntax:
sw data_source, destination_address

## Slide 18: Example
Assume $s0 contains 0x00000001 (decimal 1) and $s1 contains the memory address of an array called Mem
sw $0, 8($s1) -> store 0x00000001 in bytes 8, 9, 10, 11
Mem[8] = 0x00
Mem[9] = 0x00
Mem[10] = 0x00
Mem[11] = 0x01

## Slide 19: In Class Questions
What happens when we run the instruction sw $s3,0($s1) ?
What about sw $s3,-4($s1) ?

## Slide 20: Example Program
.data
intArr: .word 0:10
newLine: .asciiz "\n"
.text

## Slide 21: Example Program Continued
main:
#first, copy data into the array
li $t0, 0 #t0 is the loop counter
la $s0, intArr #s0 is the array address
move $t1, $s0 #t1 is the current array location
loop:
#Store the value of the loop counter + 1
add $t2, $t0, 1
sw $t2, 0($t1)
add $t1, $t1, 4
add $t0, $t0, 1
bne $t0, 10, loop #branch back to the loop tag

## Slide 22: Example Program Continued
#print the contents of the array
li $t0, 0
move $t1, $s0 #t1 is the current array location
loop2:
#load the value from the array and print it
lw $t3, 0($t1)
move $a0, $t3
li $v0, 1
syscall
#Print a new line character
la $a0, newLine
li $v0, 4
syscall
add $t1, $t1, 4
add $t0, $t0, 1
bne $t0, 10, loop2 #branch back to the loop2 tag