## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: Review of Arrays

## Slide 3: Move Instruction
lw is a "move" command.
It moves data out of memory and into registers.
Notice that integer/32-bit arrays are indexed by segments of four bytes. We can easily move through such an array.
Assume the address of our array is in $s1 and we wish to get to index 5

## Slide 4: Move Instruction
li $t1, 5 # load 5 into $t1
add $t1, $t1, $t1 # now $t1 is 10
#(it's doubled)
add $t1, $t1, $t1 # now $t1 is 20
# (it's doubled again)
add $t1, $s1, $t1 # now $t1 contains
#the address of index 5 of our array
lw $t2, 0($t1) # load the value at
# array[5] into $t2

## Slide 5: Move Instruction
Another "move" command is sw. sw moves data out of a register into memory.
sw = store word
Syntax:
  sw data_source, destination_address

## Slide 6: Example
Example Assume $s0 contains 0x00000001 (decimal 1)
sw $0, 8($s1) -> store 0x00000001 in bytes 8, 9, 10, 11
Mem[8] = 0x00
Mem[9] = 0x00
Mem[10] = 0x00
Mem[11] = 0x01

## Slide 7: Class Exercise
What happens when we run the instruction sw $s3,0($s1) ?
What about sw $s3,-4($s1) ?
As an in class exercise, we'll look at the ArrayTest.asm and IOExample.asm programs from the class website.
An aside for your homework: coverage of binary mathematics

## Slide 8: Class Exercise
We've seen how to convert from binary to decimal (multiply by 2)
1001001 = 2^0 + 2^3 + 2^6 = 1 + 8 + 64 = 73
We've seen how to convert from binary to hex
But how do we convert from decimal to binary
0 = 0
1 = 1
2 = 10
3 = 11
4 = 100 . . .

## Slide 9: Example
Notice the division by 2 method
4 % 2 = 0
2 % 2 = 0
1
The result is 100 = 1*2^2 + 0*2^1 + 0*2^0

## Slide 10: Example
Take 467
467 % 2 = 1
233 % 2 = 1
116 % 2 = 0
58 % 2 = 0
29 % 2 = 1
14 % 2 = 0
7 % 2 = 1
3 % 2 = 1
1

## Slide 11: Result
Result:
1 1101 0011
Let's check
1 D 3 hex
256 + 13*16 + 3 = 256 + 208 + 3 = 256 + 211 = 467