## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: Last Time
We looked at base 2 or binary numbers.
Let's look at some more examples of converting from decimal to binary to hex and vice versa.

## Slide 3: Binary Conversion
Given a decimal number, 576, convert it to binary. We do so by continuously taking the number modulo 2 and dividing that number in half using integer division.
576 % 2 = 0
288 % 2 = 0
144 % 2 = 0
72 % 2 = 0
36 % 2 = 0
18 % 2 = 0
9 % 2 = 1
4 % 2 = 0
2 % 2 = 0
1

## Slide 4: Binary Conversion
Then we read the binary number from bottom to top. And we can check by converting back to decimal.
1001000000b = 2^9 + 2^6 = 512 + 64 = 576
What if we want to convert 576 to hex? First, convert it to binary, then divide the binary number into groups of four bits starting from the right.
10 0100 0000
3 4 0

## Slide 5: Binary Conversion
Convert each of the groups of four bits to a hex number. Why does this work? Hex is base 16, and there are 16 possible values for four bits (2*2*2*2 = 16).
Take home message: If you need to convert a decimal number to hexadecimal, convert the decimal number to binary first.
Then, convert the binary number to hex.

## Slide 6: Binary Addition
What if we want to add two binary numbers?
Take decimal numbers 5 and 3 and add them in binary.
101b is 5 decimal
11b is 3 decimal
101
+11
-----
1000

## Slide 7: Binary Addition Contd.
Notice that there is a carry over bit. This can cause a problem called overflow. Notice that if we only have 3 bits to represent our numbers, we would have a result of zero.
Take home message: be sure to use enough precision (enough bits) to deal with the numbers you are adding
We also have to be careful with negative numbers.
We could use a one or a zero to represent the sign bit. Let's assume we have 5 bits to work with, and we try to add a positive and negative binary number. Let's use a leading one to represent a negative number and a leading zero to represent a positive number.
10011b is -3 decimal
00101b is 5 decimal

## Slide 8: Binary Addition Example
10011
+00101
-----------
11000 <---- result is -8 (wrong)
Our result should be 2 decimal. Notice that we need a different representation if we are going to directly add positive and negative numbers.
In a few days we will look at a different representation of signed integers called 2’s complement representation.
Before looking at 2's complement, we need to look at instruction formats.

## Slide 9: MIPS Instructions
MIPS instructions use 32 bits and come in 3 basic formats.
R format instructions
These are register format instructions. That is, they use only registers.
R-format instructions use the following format:
Opcode rs rt rd shamt func
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
Recall that instructions are 32-bit.
Notice that 32 = 6+5+5+5+5+6

## Slide 10: I format instructions
These are immediate format instructions. These instructions utilize a 16-bit integer value.
I-format instructions use the following format:
Opcode rs rt immediate
6 bits 5 bits 5 bits 16 bits
opcode - instruction type
rt - often the destination register
rs - often the source register
immediate - a 16 bit integer value

## Slide 11: Assembly Code Conversion
How do we convert from assembly to machine code?
Look at the green sheet in your textbook.
There are codes present near each instruction.
These codes are in hex.
For R-format instructions, the opcode is listed first, then the function code
You may ignore the shamt for now.

## Slide 12: Example
add $s1, $s2, $s5
On the green sheet, the Opcode/Funct is listed. For add it is 0 / 20_hex
0 hex in 6 bits is 000000b - our opcode
20 hex in 6 bits is 100000b - our function code
So our values follow below:
  opcode = 000000b = 0x00
  dest register (rd) = $s1 = $17 --> 0x11 --> 10001
  source register 1 (rs) = $s2 = $18 --> 0x12 --> 10010
  source register 2 (rt) = $s5 = $21 --> 0x15 --> 10101
  function value = 100000

## Slide 13: Example
The binary representation of add $s1, $s2, $s5 is:
000000 10010 10101 10001 00000 100000
opcode rs rt rd shamt func
We can easily convert this to hex by dividing our 32 bit instruction into sections of four bits and finding the hex value for each set of four bits.
0000 0010 0101 0101 1000 1000 0010 0000 --> 0x02558820

## Slide 14: Recap
Notice that we can now represent binary numbers in multiple ways.
They could be an address, ASCII text, instructions (I or R format), a signed number, unsigned numbers, or floating point numbers.
Instruction formats are an encoding that allows us to represent our instructions as numbers.