## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: Last Time
Basic binary mathematics
R format and I format instructions

## Slide 3: Recall
What if we want to add two binary numbers?
Take decimal numbers 5 and 3 and add them in binary.
  101b is 5 decimal
  11b is 3 decimal
101
+ 11
-----
1000
Notice that there is a carry over bit. This can cause a problem called overflow. Notice that if we only have 3 bits to represent our numbers, we would have a result of zero.

## Slide 4: Recall
We also have to be careful with negative numbers.
We could use a one or a zero to represent the sign bit. Let's assume we have 5 bits to work with, and we try to add a positive and negative binary number.
10011b is -3 decimal
00101b is 5 decimal
10011
+ 00101
-----------
11000 <---- result is -8 (wrong)
Our result should be 2 decimal. Notice that we need a different representation if we are going to directly add positive and negative numbers.
In a few days we will look at a different representation of signed integers called 2's complement representation.

## Slide 5: MIPS Instructions
MIPS instructions use 32 bits and come in 3 basic formats.
R format instructions
  These are register format instructions. That is, they use only registers.
R-format instructions use the following format:
opcode rs rt rd shamt func
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
Notice: 32 = 6+5+5+5+5+6
The opcode represents the instruction type.
The func or function code allows for specification of a variant of the operation in the opcode (e.g. a math or ALU function)
  rs - the first source register
  rt - the second source register
  rd - the destination register
  shamt - the shift amount (used for bit shifting)

## Slide 6: I Instructions
I format instructions
These are immediate format instructions. These instructions utilize a 16-bit integer value.
I-format instructions use the following format:
opcode rs rt immediate
6 bits 5 bits 5 bits 16 bits
  opcode - instruction type
  rt - often the destination register
  rs - often the source register
  immediate - a 16 bit integer value

## Slide 7: Various Instruction Formats
So far we have seen many basic programming elements within the MIPS instruction set.
We have seen the following:
Arrays
Input/Output operations
Mathematical operations
Notice that many of these use R or I format instructions. For example,
  add $t1, $t2, $t3
  sub $t1, $t2, $t3
  mul $t1, $t2, $t3
  div $t1, $t2, $t3
Are all R-format instructions

## Slide 8: Various Instruction Formats
addi $s1, $s2, 100
lw $s2, -8($s1)
sw $t3, 102($s6)
Are all I format instructions.
Similarly, there are floating point instructions with the same format.
Recall from Java that there are both single and double precision variables.

## Slide 9: Floating Point Registers
MIPS floating point registers are provided in Coprocessor 1. There are 32, 32-bit, single precision floating point registers.
These registers are provided in the following format:
$f0, $f1, $f2, . . .$f31
Pairs of single precision registers are used to represent double precision (64 bit) floating point numbers.
There are 16 double precision floating point registers. These are represented using pairs of floating point registers starting with an even numbered register.
E.g. the pair $f0 and $f1 is represented using $f0. The list of registers is provided below.
$f0, $f2, $f4. . . .$f30

## Slide 10: Floating Pt. Operations
Floating point operations instructions have almost exactly the same name as their integer counterparts.
Often these operations are in the format instruction_name.d for double precision operations or instruction_name.s for single precision operations.
Examples of such operations follow below.
add.s $f1, $f2, $f3 add.d $f2, $f4, $f6
sub.s $f1, $f2, $f3 sub.d $f2, $f4, $f6
mul.s $f1, $f2, $f3 mul.d $f2, $f4, $f6
div.s $f1, $f2, $f3 div.d $f2, $f4, $f6
mov.s $f2, $f3 mov.d $f2, $f4
# move contents of one
# double register to another

## Slide 11: Example
Examples of array allocation for double or single precision values are provided below.
  myFloatArray: .single 1.1, 2.2, 3.3
  myDoubleArray: .double 4.4, 5.5, 6.6, 7.7
Space may be allocated for arrays of fixed size as follows:
  myFloatArray: .single 0:200
  myDoubleArray: .double 0:100
Where size and initialization value are provided in the format init_value:size.

## Slide 12: MIPS Operations
To load and store values, the pseudo-instructions l.d, l.s, s.d, and s.s may be used to load and store double and single precision floating point numbers.
We will investigate their use in the next lecture.
But we are missing something. We've seen I/O, arrays, and mathematical operations.
We have not seen details on logical, comparison, or branching operations yet.

## Slide 13: Branching Operations
There are two basic branching operations:
  beq - branch if equal
  bne - branch if not equal
These instructions are provided in the following format:
  beq $t1, $t2, label
  bne $t1, $t2, label
These compare whether $t1 and $t2 are equal or not. That is they look for either a true or a false value.
Provided a comparison operator, these are actually all we need to accomplish loops and if-then-else statements.
There are other operators, but we'll only investigate these for now.

## Slide 14: Branching Examples
Take a if statement as an example:
  if($t1 == $t2)
  {
  //do something
  }
We can represent this if statement in MIPS as follows:
  bne $t1, $t2, endif
  # do something
  endif:
Notice that we branch to label "endif:" if $t1 != $t2.
That is, we ignore the segment of code where we "do something".

## Slide 15: Example
Similarly for a loop we can use a label, What if we have the following loop:
  do {
  //do loop operations
  } while (t1 == t2);
Where the loop continues so long as t1 == t2. This code may be represented in MIPS as follows:
  loopStart:
  #do loop operations
  beq $t1, $t2, loopStart
Notice that if t1 == t2, we return to the beginning of the loop.
Otherwise, we drop past the end of the loop and continue processing from that point.

## Slide 16: Comparison Operations
We would like to compare values using operators such as >, <, >=, or <=.
We actually only need one of these operators to perform comparisons. This is the < operator. This is provided by the "slt" instruction. There are also pseudo-instructions like the "sle" instruction that provide functionality for other comparisons like <= without the need to modify the operands.
The slt and sle instructions allow us to set a register to true or false depending upon the result of comparing two registers.

## Slide 17: Comparison Operations
These instructions use the following format:
  slt $t1, $t2, $t3
  sle $t1, $t2, $t3
Where t1 is set to true if t2 < t3 or t2 <= t3, respectively.
Given a true or false (i.e. a one or zero) result from one of these instructions, we can use the result in a branching operation.
For example, the code below implements an if statement that does work if t2 < t3
  slt $t1, $t2, $t3
  beq $t1, $zero, myLabel
  # do work
  myLabel:
We will look at more floating point, branching, and comparison operations next time.