## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: Last Time
R, I, and J Format instructions
Start on floating point operations
Start on branching operations
Start on comparison operations
This time we will continue coverage of those topics and review examples

## Slide 3: J format instructions
These are jump format instructions.
They utilize a 6 bit opcode and a 26 bit integer address.
J-format instructions using the following format:
  opcode address
  6 bits 26 bits
or
  instruction label
Examples of this include the following jump operations:
  j label
  jal label
The "j" instruction means jump directly to a label.
There is no return address provided when using this instruction.
The "jal" instruction means jump and link.
With "jal", a return address is stored in the $ra register so you may return from a call.

## Slide 4: J Format
Jump format instructions are often used for subroutine (method) calls. We will discuss subroutines next week.
Notice that J-format instructions allow us to move backward or forward in memory by as many as 2^25 instructions. This allows for a very large program size.

## Slide 5: Branching Instructions
Recall from the previous lecture that there are two basic branching operations:
  beq - branch if equal
  bne - branch if not equal
These instructions are provided in the following format:
  beq $t1, $t2, label
  bne $t1, $t2, label
These compare whether $t1 and $t2 are equal or not. That is they look for either a true or a false value.
Provided a comparison operator, these are actually all we need to accomplish loops and if-then-else statements.
There are other operators, but we'll only investigate these for now.

## Slide 6: Comparison Instructions
Additionally, recall from the previous lecture that we would like to compare values using operators such as >, <, >=, or <=.
We actually only need one of these operators to perform comparisons. This is the < operator.
This is provided by the "slt" instruction.
There are also pseudo-instructions like the "sle" instruction that provide functionality for other comparisons like <= without the need to modify the operands.
  slt - store less than
  sle - store less than or equal
The slt and sle instructions allow us to set a register to true or false depending upon the result of comparing two registers.
The destination register is set to the truth value of the result of comparing the two operand registers.
These instructions use the following format:
  slt $t1, $t2, $t3
  sle $t1, $t2, $t3
Where t1 is set to true if t2 < t3 or t2 <= t3, respectively.

## Slide 7: Examples
Take a if statement in Java or C as an example:
  if(x < y) {
  //do something
  }
  //do something else
If we represent x as $t1 and y as $t2, we can compare x and y using slt. Let’s store the result in $t3.
  slt $t3, $t1, $t2
Notice that we want to execute the "do something" statements if the comparison is true and then "do something else”.
If the comparison is false, we want to only "do something else".
This means if the comparison is false we need to jump past the statements where we "do something”.
That is, we need to branch if "x < y" is false, or if $t3 == 0.
We can use the bne instruction to accomplish this.

## Slide 8: Examples
slt $t3, $t1, $t2
#store the truth value of x < y in $t3
beq $t3, $zero, endif
#do something (our if instructions go here)
endif:
#do something else (the instructions after the if go
#here)
Let's make the example more concrete.
Assume we want to print something if x < y.
Let's assume we have the following strings in the .data section:
xLTy: .asciiz "X is less than Y\n"
afterIf: .asciiz "After the if statement\n"

## Slide 9: Example
Given our previous example it makes sense to print xLTy within the if statement, and to print afterIf, after the if statement. If we incorporate these into our code, it looks like this:
    slt $t3, $t1, $t2 #store the truth value of x < y in $t3
    beq $t3, $zero, endif
    #do something (our if instructions go here)
    li $v0, 4 #print xLTy
    la $a0, xLTy
    syscall
    endif: #do something else (the instructions after the if go here)
    li $v0, 4
    la $a0, afterIf
    syscall

## Slide 10: Example
What if we want to use a loop? Assume we have the following loop:
    do {
    //do loop operations
    i++;
    System.out.println(i);
    } while (i < n);
Where the loop continues so long as x < y.
Let's assume i is stored as $t1 and n is stored as $t2.
This code may be represented in MIPS as follows on the next slide.

## Slide 11: Example
.data
newLine: .asciiz "\n"
.text
main:
#initialization values go here
do:
#do loop operations
  addi $t1, $t1, 1
  li $v0, 1 #print i or $t1
  move $a0, $t1 #copy contents of $t1 into $a0
  syscall
  li $v0, 4 #print a newline character
  la $a0, newLine
  syscall
slt $t3, $t1, $t2
bne $t3, $zero, do

## Slide 12: Loop
Notice that if x < y or $t1 < $t2, $t3 is true or not equal to zero.
We return to the beginning of the loop as long as $t3 is not equal to zero.
Otherwise, we drop past the end of the loop and continue processing from that point.
What if we want a while loop instead of a do-while?
Notice that a while loop is simply a do-while where we check the condition first.
So, we can modify our code to create the following while loop by checking our condition before entering the loop:

## Slide 13: Example
while(i < n)
{
//do loop operations
i++;
System.out.println(i);
}

## Slide 14: Assembly code
.data
newLine: .asciiz "\n"
.text
main: #initialization values go here
slt $t3, $t1, $t2
beq $t3, $zero, endwhile
do: #do loop operations
  addi $t1, $t1, 1
  li $v0, 1 #print i or $t1
  move $a0, $t1 #copy contents of $t1 into $a0
  syscall
  li $v0, 4 #print a newline character
  la $a0, newLine
  syscall
slt $t3, $t1, $t2
bne $t3, $zero, do
endwhile: #continue processing after the loop

## Slide 15: Logical Operations
Notice that we check if the condition i < n is false first. If so, we bypass the loop.
We'll look at how to simplify this code in a later lecture.
More logical operations
  We've seen how to do comparisons and branching, but what if we want to evaluate the truth value of multiple comparisons in the same if or while statement?
  We need the logical operators && (and) and || (or) from Java/C.
  MIPS implements these operations using the instructions "and" and "or".

## Slide 16: Logical Operations
Both of these are R-format instructions. That is, we represent "and" and "or“ with the following format:
  and $t1, $t2, $t3
  or $t4, $t2, $t3
The result is the truth values of "$t2 && $t3" and "$t2 || $t3" are stored in $t1 and $t4, respectively.
We can make comparisons such as x < y || y < z easily by using multiple instructions.

## Slide 17: Logical Operations
For example, assume x is $t1, y is $t2, and z is $t3. We can obtain the truth values of our comparisons x < y and y < z as follows:
  slt $t4, $t1, $t2 # x < y
  slt $t5, $t2, $t3 # y < z
Now we can compute the truth value of x < y || y < z by finding the "or" result of $t4 and $t5.
  or $t6, $t4, $t5
Similarly, if we wanted the result of x < y && y < z we could use the "and" instruction.
  and $t6, $t4, $t5
Next time we will look at more examples of comparisons and logical operations, and we will look at floating point operations.