## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: Program Review
Review of floating point mathematics for the next project using FPMath.asm

## Slide 3: Review Contd.
Double values to be stored in memory are declared and initialized in the .data section.
x: .double 18.2
y: .double 34.6
small: .double 0.000000000000001
Single precision values may be declared and initialized in the same manner.
z: .float -2.3

## Slide 4: Load Instructions
Double and single precision values may be loaded into memory using the l.d and l.s instructions, respectively.
l.d $f2, x
l.d $f4, y
l.d $f18, small
l.s $f17, z
Floating point mathematics operations are carried out using the same instruction name except with a .d or .s at the end.

## Slide 5: Floating Point Instructions
Examples of double mathematics instructions follow below.
    add.d $f6, $f2, $f4
    sub.d $f8, $f2, $f4
    div.d $f10, $f2, $f4
    mul.d $f14, $f2, $f4
Examples of single precision mathematics operations follow below.
    add.s $f16, $f17, $f21
    sub.s $f16, $f17, $f21
    div.s $f16, $f17, $f21
    mul.s $f16, $f17, $f21

## Slide 6: Floating Point Instructions
Additionally, it is possible to move floating point values from one register to another using the mov.d or mov.s instructions.
The destination is specified first, and the source is specified last.
mov.d $f12, $f14
mov.s $f0, $f1

## Slide 7: Floating Instructions
There are also system call codes to read and write double and single precision values to and from the console.
  li $v0, 3 # print a double value stored in $f12
  syscall
  li $v0, 2 # print a float value stored in $f12
  syscall
  li $v0, 7 # read a double into $f0
  syscall
  li $v0, 6 # read a float into $f0
  syscall

## Slide 8: Floating Pt. Registers
It is possible to move values back and forth between floating point registers and integer registers.
  mfc1 $t1, $f1 #move value from $f1 in co-proc. 1 to $t1
  #in co-proc. 0
  mtc1 $f1, $t1 #move value from $t1 in co-proc. 0 to $f1
  #in co-proc. 1
It is also possible to convert to and from double, single, and word formats using the cvt.x.y instruction where x and y are replaced with s, d, or w for float, double, or integer respectively.
  cvt.d.w $f16, $f1 #convert from word to double
  cvt.s.w $f16, $f1 #convert from word to float
  cvt.w.d $f1, $f2 #convert from double to word
  cvt.w.s $f1, $f2 #convert from float to word

## Slide 9: Floating Point Instructions
Comparing double or float values requires the use of the less than or greater than operator and the absolute value (abs.d) operator as we can't use an equals operator to compare double values.
  #print the truth results of x == y
  #need abs(x - y) < 0.000000000000001
  abs.d $f16, $f8 # $f8 contains x - y
  c.lt.d $f8, $f18 #set condition flag zero if abs(x - y) < small value
Comparison results are stored in the coprocessor 1 condition flag. We can branch if the condition flag is true by using bc1t.
We can branch if the condition flag is false using bc1f. These instructions use the following format:
    bc1f label
    bc1t label

## Slide 10: Example Program
An example of the use of the bc1f instruction follows below.
bc1f else
if: #if abs(x-y) < 0.000000000000001
  li $v0, 4
  la $a0, xLTy
  syscall
  #beq $zero, $zero, endif works as well
  b endif
else:
  li $v0, 4
  la $a0, xGTEy
  syscall
endif:
li $v0, 10 #end program
syscall

## Slide 11: Example
.data
newLine: .asciiz "\n"
.text
main:
#initialization values go here
do:
#do loop operations
  addi $t1, $t1, 1
  li $v0, 1 #print i or $t1
  move $a0, $t1 #copy contents of $t1 into $a0
  syscall
  li $v0, 4 #print a newline character
  la $a0, newLine
  syscall
slt $t3, $t1, $t2
bne $t3, $zero, do

## Slide 12: Iteration Recap
Notice that if x < y or $t1 < $t2, $t3 is true or not equal to zero. We return to the beginning of the loop as long as $t3 is not equal to zero.
Otherwise, we drop past the end of the loop and continue processing from that point.
What if we want a while loop instead of a do-while?
Notice that a while loop is simply a do-while where we check the condition first.
So, we can modify our code to create the following while loop by checking our condition before entering the loop:

## Slide 13: Example
while(i < n)
{
//do loop operations
i++;
System.out.println(i);
}

## Slide 14: Assembly code
.data
newLine: .asciiz "\n"
.text
main: #initialization values go here
slt $t3, $t1, $t2
beq $t3, $zero, endwhile
do: #do loop operations
  addi $t1, $t1, 1
  li $v0, 1 #print i or $t1
  move $a0, $t1 #copy contents of $t1 into $a0
  syscall
  li $v0, 4 #print a newline character
  la $a0, newLine
  syscall
slt $t3, $t1, $t2
bne $t3, $zero, do
endwhile: #continue processing after the loop

## Slide 15: Logical Operations
Notice that we check if the condition i < n is false first. If so, we bypass the loop.
We'll look at how to simplify this code in a later lecture.
More logical operations
  We've seen how to do comparisons and branching, but what if we want to evaluate the truth value of multiple comparisons in the same if or while statement?
  We need the logical operators && (and) and || (or) from Java/C.
  MIPS implements these operations using the instructions "and" and "or".

## Slide 16: Logical Operations
Both of these are R-format instructions. That is, we represent "and" and "or“ with the following format:
  and $t1, $t2, $t3
  or $t4, $t2, $t3
The result is the truth values of "$t2 && $t3" and "$t2 || $t3" are stored in $t1 and $t4, respectively.
We can make comparisons such as x < y || y < z easily by using multiple instructions.

## Slide 17: Logical Operations
For example, assume x is $t1, y is $t2, and z is $t3. We can obtain the truth values of our comparisons x < y and y < z as follows:
  slt $t4, $t1, $t2 # x < y
  slt $t5, $t2, $t3 # y < z
Now we can compute the truth value of x < y || y < z by finding the "or" result of $t4 and $t5.
  or $t6, $t4, $t5
Similarly, if we wanted the result of x < y && y < z we could use the "and" instruction.
  and $t6, $t4, $t5
Next time we will look at more examples of comparisons and logical operations, and we will look at floating point operations.