## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: Review
Last time we began coverage of Boolean Algebra.

## Slide 3: Boolean Laws
We have been using ~ to represent NOT, * to represent AND, and + to represent OR.
We covered the following laws from Boolean Algebra:
  NULL Laws: A*0 = 0 A+1 = 1
  Idempotency: A*A = A A+A = A (Doesn't change result)
  Complement Laws: A + ~A=1 A*~A = 0
  Identity Laws: A+0 = A A*1 = A
  Involution: ~~A = A (Double negation)
  Commutative Laws: A+B = B+A A*B = B*A
  Associative Laws: A+(B+C) = (A+B)+C A*(B*C) + (A*B)*C
  Distributive Laws: A*(B+C) = A*B + A*C A+(B*C) = (A+B) * (A+C)
  Covering Law: B*(B+C) = B + B*C = B
  Combining: B*C + B * ~C = B (B+C) * (B + ~C) = B

## Slide 4: Understanding LittleFe
LittleFe's head node controls the child nodes when running distributed programs – those that may be broken up into multiple tasks and sent to many computers.
Some distributed programs require much network communication while others don't.
Let's consider the N-Body problem.
  This is a problem where we have N entities (we'll pretend they are stars) that all exert forces on each other.
  To figure out how these stars will move, we need to determine all the forces each star exerts on every other star.
  Physics tells us that if we sum up all the forces on each of the stars, we can determine the acceleration of the stars, as long as we know their masses.
  So, the N-Body problem is a O(n^2) problem (read as big Oh of n squared).

## Slide 5: LittleFe Contd.
If we have lots of processors, we can speed up the program significantly, but communication is required if we divide the problem between different computers.
Notice that if 5 stars are on computer 1 and 6 stars are on computer 2, we must send the forces exerted on each group from one computer to another over a network interface.
Network interfaces are much slower than memory.
Common network speeds are 100 Megabits/second and 1 Gigabit/second. These are about 12.5 Megabytes/sec and 125 Megabytes/second respectively.
Common bus speeds between CPU and Memory
Additionally, there is network latency. Latency with respect to sending a message from one computer to another is the overhead to send a message with no data. This is the amount time we must wait before we are able to process any data when sending a message.

## Slide 6: LittleFe Contd.
For LittleFe sending a message from one motherboard to another involves creating a network link from one computer to another over a single network switch.
So, the initial time cost of creating such a link is the time for the switch and both motherboards to acknowledge that such a connection has been created.
This time is likely several milliseconds.
While communication between nodes (motherboards) is useful, we can make the best use of our resources by doing as much computation on each node as possible and limiting communication.
So if we have 1000 stars, we might send 1000/6 stars to each of the six nodes on LittleFe to divide up the work.

## Slide 7: Boolean Algebra
Recall that OR is a binary operation that is true if either part is true OR is called a disjunction and is represented by a |, ||, V, or + symbol.
Recall that AND is a binary operation that is true only if both parts are true AND is called a conjunction and is represented by a carat (^), &, &&, or * symbol.
Truth tables
X Y X + Y X Y X * Y
---------------------- -------------------------
F F F F F F
F T T F T F
T F T T F F
T T T T T T

## Slide 8: Boolean Algebra
Recall that OR is a binary operation that is true if either part is true OR is called a disjunction and is represented by a |, ||, V, or + symbol.
Recall that AND is a binary operation that is true only if both parts are true AND is called a conjunction and is represented by a carat (^), &, &&, or * symbol.
Recall that NOT negates a binary value. NOT is represented as a ~, !, notch, or / symbol
Truth tables
X Y X + Y X Y X * Y X ~X
---------------------- ------------------------- --------------------
F F F F F F T F
F T T F T F F T
T F T T F F
T T T T T T

## Slide 9: More Boolean Algebra
Other operations such as XOR (exclusive or), NAND (not and), and NOR (not or) can be represented by combining the operations above.
In Java, & represents a bitwise AND, and | represents a bitwise OR. These are equivalent to the "and" and "or" instructions MIPS.
0111
&1001
---------
0001
1011
|0010
--------
1011

## Slide 10: More Boolean Algebra
Other operations such as XOR (exclusive or), NAND (not and), and NOR (not or) can be represented by combining the operations above.
In Java, & represents a bitwise AND, and | represents a bitwise OR. These are equivalent to the"and" and "or" instructions MIPS.
0111
&1001
---------
0001
1011
|0010
--------
1011
Notice that these are different than the logical && and || operators.

## Slide 11: Boolean Algebra Rules
Boole's Laws:
  NULL Laws: A*0 = 0 A+1 = 1
  Idempotency: A*A = A A+A = A (Doesn't change result)
  Complement Laws: A + ~A=1 A*~A = 0
  Identity Laws: A+0 = A A*1 = A
  Involution: ~~A = A (Double negation)
  Commutative Laws: A+B = B+A A*B = B*A
  Associative Laws: A+(B+C) = (A+B)+C A*(B*C) + (A*B)*C
  Distributive Laws:
    A*(B+C) = A*B + A*C
    A+(B*C) = (A+B) * (A+C)
  Covering Law: B*(B+C) = B + B*C = B
  Combining: B*C + B * ~C = B (B+C) * (B + ~C) = B
  Precedence: NOT, AND, OR

## Slide 12: Rules
DeMorgan's Laws for converting from ANDs to ORs:
~(A * B) = ~A + ~B
~(A + B) = ~A * ~B
These generalize:
~(A + B + C) = ~A * ~B * ~C
We can use these laws to simplify nasty equations:
( (A*B) + (A*C) + (B*C) ) * ~(A*B*C)= ( (A*B) + (A*C) + (B*C) ) * (~A + ~B + ~C) by DeMorgan's Law
= (A*B)* (~A + ~B + ~C) + (A*C)* (~A + ~B + ~C) + (B*C)* (~A + ~B + ~C) by distribution
= A*B*~A + A*B*~B + A*B*~C + A*C*~A + A*C*~B + A*C*~C + B*C*~A + B*C*~B + B*C*~C
= 0*B + 0*A + A*B*~C + 0*C + A*C*~B + A*0 + B*C*~A + 0*C + 0*B by inverse law
= 0 + 0 + A*B*~C + 0 + 0 + A*C*~B + 0 + 0 + B*C*~A by null law
= A*B*~C + A*C*~B + B*C*~A by identity law
= A*B*~C + A*~B*C + ~A*B*C by commutative law

## Slide 13: Propagation Delay
Note that gates are made from relays and/or transistors
These are AND, OR, NOT, XOR, NOR, NAND, and many others.
Gates are mechanical devices. It takes time for information to travel through them. This time is called propagation delay
Physical arrangement of these gates creates specific orders of operations
For example B*C+A
Propagation delay is the time it takes for information (a signal) to pass through a gate or series of gates.
Propagation delay determines the maximum clock speed.
If it takes 15ns for data to pass through a series of gates, the clock speed cannot be faster than 66 MHz

## Slide 14: Equation Styles
Sum of Products (SOP) - A*C + B*C + A*D + B*D
Product of Sums (POS) - (A+B) * (C+D)
Truth table
A B C D AC BC AD BD AC+BC+AD+BD A+B C+D (A+B)*(C+D)
0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 1 0 0 0 0 0 0 1 0
0 0 1 0 0 0 0 0 0 0 1 0
0 0 1 1 0 0 0 0 0 0 1 0
0 1 0 0 0 0 0 0 0 1 0 0
0 1 0 1 0 0 0 1 1 1 1 1
0 1 1 0 0 1 0 0 1 1 1 1
0 1 1 1 0 1 0 1 1 1 1 1
1 0 0 0 0 0 0 0 0 1 0 0
0 0 1 0 0 1 0 1 1 1 1
1 0 1 0 1 0 0 0 1 1 1 1
0 1 1 1 0 1 0 1 1 1 1
1 1 0 0 0 0 0 0 0 1 0 0
1 0 1 0 0 1 1 1 1 1 1
1 1 1 0 1 1 0 0 1 1 1 1
1 1 1 1 1 1 1 1 1 1 1
Notice that (A+B)*(C+D) is equivalent to AC+BC+AD+BD