## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patternson and Hennessy Text

## Slide 2: JLS
JLS will be reviewed using in-class examples
An example of an AND gate can be found on the example code page.
This example is in a zip file and is called SimpleAnd.jls
Students will need to download JLS from the links page of the course website.

## Slide 3: Instructions for JLS “Simple And” Example
Be sure to right click on the signal generator in the example, and click "Modify". This will show you the signals that are being generated over time.
Notice that the syntax a JLS signal generator follows below. If your truth table looks like:
A B A*B
-------------
0 0 0
0 1 0
1 0 0
1 1 0

## Slide 4: JLS Signal Generator
Then your JLS signal generator code should be:
A 0 for 50
0 for 50
1 for 50
1 for 50
0
end
B 0 for 50
1 for 50
0 for 50
1 for 50
0
end
Stopper 0 for 400
1
end

## Slide 5: Simple And Example, Continued
After opening SimpleAnd.jls in JLS, you can run a simulation by first clicking “Simulator”, then clicking “Show Simulator Window”.
Next, you can click start to show the simulation.
If you make your own circuit, you will need to right-click on the inputs and outputs and click "Watch Element" to see the values of each element over time in the simulator frame.

## Slide 6: Exam Review
For the exam, it is highly recommended that you review and understand the following information:
Understanding what a bit and a byte consists of and the composition of data types in bits and bytes.
MIPS Floating Point Operations including comparisons, mathematics, loading, and storing data.

## Slide 7: MIPS
MIPS Assembly for Integer and character operations including the following:
  system calls
  registers
  basic instructions such as loading, storing, mathematics, logic operations, etc.
  if statements, loops
  functions

## Slide 8: Boolean Algebra
Boolean Algebra basics including the following:
NULL Laws: A*0 = 0 A+1 = 1
Idempotency: A*A = A A+A = A (Doesn't change result)
Complement Laws: A + ~A=1 A*~A = 0
Identity Laws: A+0 = A A*1 = A
Involution: ~~A = A (Double negation)
Commutative Laws: A+B = B+A A*B = B*A
Associative Laws: A+(B+C) = (A+B)+C A*(B*C) + (A*B)*C
Distributive Laws:
  A*(B+C) = A*B + A*C
  A+(B*C) = (A+B) * (A+C)
Covering Law: B*(B+C) = B + B*C = B
Combining: B*C + B * ~C = B (B+C) * (B + ~C) = B

## Slide 9: Conversions
Converting from MIPS instructions to binary and to hexadecimal.
Conversions from decimal numbers to binary two's complement numbers.
Two's complement arithmetic.
Converting from real decimal numbers (floating point) to binary floating point numbers.

## Slide 10: Computer Components
Understand the Fetch-Decode-Execute Cycle (how instructions are retrieved from memory, how the control unit decides where they go, and how they are processed) and the following CPU components and computer components:
  Control Unit
  Program Counter
  Registers
  ALU Memory
  Disk (Secondary Memory)