## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patterson and Hennessy Text

## Slide 2: Review
Adders/Review of programming project

## Slide 3: Adders
How to perform one bit addition - a half adder
Assume we are given two variables, A and B that each represent a bit (a one or a zero). To create a logic circuit that will add two such variables, we need the following:
Inputs for A and B and at least one output.
Let's enumerate all the possibilities (here the plus symbol represents addition, not the OR operation):
If A = 0 and B = 0, 0 + 0 = 0b
If A = 0 and B = 1, 0 + 1 = 0b
If A = 1 and B = 0, 1 + 0 = 1b
If A = 1 and B = 1, 1 + 1 = 10b
Notice that we need two bits for our output. We will call the extra bit a "Carry out". In the truth table below, the carry out is represented as C_O.

## Slide 4: Truth Table
A B C_O Output
--------------------------------------
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0
Notice that we can create a pair of equations for the truth table above using the sum of products method.
C_O = A*B
Output = ~A*B + A*~B
The equations above only form a half adder, though.

## Slide 5: Example
Consider the case where we add more than one bit.
Let's look at an example:
Given two binary numbers, 11b and 11b, add them and determine the result:
1 <---- Carry in bit
  11
+11
-----
110
Notice that the result of 11b + 11b or 3 + 3 is 110b or 6.
Observe that there is one bit that is both carried out from the first addition and carried in to the second addition.
A full one bit adder must account for both a carry in bit and a carry out bit.

## Slide 6: 4 bit Adder
Instead of four equations, we have eight to deal with. We will use C_I to represent the carry in bit and C_O to represent the carry out bit.
Assume A = 0, B = 0, C_I = 0, then 0 + 0 + 0 = 00
Assume A = 0, B = 1, C_I = 0, then 0 + 1 + 0 = 01
Assume A = 1, B = 0, C_I = 0, then 1 + 0 + 0 = 01
Assume A = 1, B = 1, C_I = 0, then 1 + 1 + 0 = 10
Assume A = 0, B = 0, C_I = 1, then 0 + 0 + 1 = 01
Assume A = 0, B = 1, C_I = 1, then 0 + 1 + 1 = 10
Assume A = 1, B = 0, C_I = 1, then 1 + 0 + 1 = 10
Assume A = 1, B = 1, C_I = 1, then 1 + 1 + 1 = 11

## Slide 7: Truth Table
So our truth table appears as follows for a full adder:
A B C_I C_O Output
-------------------------------------
0 0 0 0 0
0 1 0 0 1
1 0 0 0 1
1 1 0 1 0
0 0 1 0 1
0 1 1 1 0
1 0 1 1 0
1 1 1 1 1
Now, the equations for C_O and Output are as follows:
C_O = A*B*~C_I + ~A*B*C_I + A*~B*C_I + A*B*C_I
Output = ~A*B*~C_I + A*~B*~CI + ~A*~B*C_I + A*B*C
Logic gates in JLS format are provided for these equations on the examples page of the class website