## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patterson and Hennessy Text

## Slide 2: Review
We continued review of the JLS files for adders using logic gates as provided on the examples page.

## Slide 3: Adders
Notice that the adder itself is a modular component. We can abstract upon the concept of an adder, considering it to be a black box, since we already know how to implement the logic. The diagram below is an example of such an abstraction.
+----------------+
-| A C_O |-
| |
-| B Out |-
| |
-| C_I |
+----------------+
So, in the diagram above, we have our inputs A, B and C_In and our outputs C_O and Out. We pretend that the box contains the logic to implement a one-bit adder.

## Slide 4: Adders
Notice that we may join two adders together by providing the carry out of the first as the carry in for the second. Doing so provides a two bit adder that produces outputs Out1, Out2, and C_O_2 from inputs A1, A2, B1, and B2.
Additionally, notice that joining two adders providing the carry out, C_O_1 from the first adder as the carry in to the second adder, C_I_2, provides for a two-bit adder as shown on the example page of the class website.
For an adder, the least significant bit always takes a carry-in of zero.
Notice that an adder provides one of the key features necessary for our CPU - addition (i.e. part of the ALU).

## Slide 5: RS-Latches
An example of a reset-set or RS latch is provided on the examples page of the class website.
An RS latch provides the capability to store one bit and provide an output.
This latch consists of two NOR (not or) gates.
One gate has an input R, that when true resets the value stored in the latch to zero.
The other gate has an input S, that when true sets the value stored in the latch to one.

## Slide 6: RS Latches
The outputs of the gates are the stored value Q, which is output from the gate having R as an input, and the inverse of the stored value ~Q, which is output from the gate having S as an input.
The outputs are fed back as inputs into the pair of NOR gates.
Q is fed into the same gate as S.
~Q is fed into the same gate as R.
Next time we will look at the various states of the RS Latch.