## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patterson and Hennessy Text

## Slide 2: Review
Last time we looked at RS Latches
Today we are going to see how the RS latch is related to memory latency based upon its steady state responses.
We will investigate this on the board and using JLS.

## Slide 3: RS Latch
Consider the possible correct states for the RS latch:
Correct states are when Q = 1 and ~Q = 0 or
when Q = 0 and ~Q = 1
Partial truth tables for these states are listed below:
Assume both R and S are false. Q and ~Q should not change in this case.
Q ~Q R S | ~(~Q+R)=Q ~(Q+S)=~Q
------------------------------+--------------------------------------
0 1 0 0 | 0 1
1 0 0 0 | 1 0
Notice that for the first line in the truth table above:
~(~Q + R) = ~(1+0) = ~1 = 0 and ~(Q+S) = ~(0+0) = 1, so the first line is correct.
Notice that for the second line in the truth table above:
~(~Q + R) = ~(0+0) = ~0 = 1 and ~(Q+S) = ~(1+0) = 0, so the second line is correct.

## Slide 4: RS Latch contd.
Assume we are performing a reset. R is one in this case. Q should always change to zero and ~Q to one.
Q ~Q R S | ~(~Q+R)=Q ~(Q+S)=~Q
------------------------------+--------------------------------------
0 1 1 0 | 0 1
1 0 1 0 | 0 1
Notice that for the first line in the truth table above:
~(~Q + R) = ~(1+1) = ~1 = 0 and ~(Q+S) = ~(0+0) = 1, so the first line is correct.
Notice that for the second line in the truth table above:
~(~Q + R) = ~(0+1) = ~1 = 0 and ~(Q+S) = ~(1+0) = 0, so the second line has an issue.
If we assume it takes the same amount of time for data to pass through the gates, let's find out what happens.

## Slide 5: RS-Latches
Assume the 2 zeroes propagate back through the gates again, now our equations are as follows:
~(~Q + R) = ~(0+1) = ~1 = 0 = Q <-- this is ok
~(Q + S) = ~(0+0) = ~0 = 1 = ~Q <-- this is ok, too
So, it takes extra time for the data to stabilize.
This wait time is also referred to as latency.

## Slide 6: RS Latches
Now assume that we are performing a set. S is one in this case. Q should always change to one and ~Q to zero.
Q ~Q R S | ~(~Q+R)=Q ~(Q+S)=~Q
------------------------------------+--------------------------------------
0 1 0 1 | 1 0
1 0 0 1 | 1 0
Notice that for the second line in the truth table above:
~(~Q + R) = ~(0+0) = ~0 = 1 and ~(Q+S) = ~(1+1) = 0, so the second line is correct.
Notice that for the first line in the truth table above:
~(~Q + R) = ~(1+0) = ~1 = 0 and ~(Q+S) = ~(0+1) = 0, so the first line initially produces incorrect output.
If we assume it takes the same amount of time for data to pass through the gates, let's find out what happens.

## Slide 7: RS Latches
Assume the 2 zeroes propagate back through the gates again, now our equations are as follows:
~(~Q + R) = ~(0+0) = ~0 = 1 = Q <-- this is ok
~(Q + S) = ~(0+1) = ~1 = 0 = ~Q <-- this is ok, too
So, again it takes extra time for the data to stabilize.
Performing both a set and a reset at the same time is an invalid operation and will result in an oscillating state. It is possible to recover from this state by attempting to set and reset the latch, but it will take time to recover.

## Slide 8: D Latch
We would like to prevent oscillating states from ever occurring. This can be accomplished with a more complex latch called a D-latch and with a D-flip-flop. These are built using RS-latches.
So far we have several of the components we need to create a CPU. Latches will allow us to create registers, and adders are part of our ALU.
With the addition of a memory, a clock, multiplexors and decoders, we can implement the fetch-decode-execute cycle.