## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patterson and Hennessy Text

## Slide 2: Review
Finishing Flip Flops
Last time we looked at the D-Latch and investigated how it prevents an RS-latch from entering a state in which both set and reset are true.
We also investigated both gate and component based diagrams of the D-Latch

## Slide 3: More Flip Flops
Ideally we would like storage devices such as registers to become active with the rising edge of a clock signal.
Computers run on a system clock that utilizes a constant frequency.
Given a constant frequency such as 1 GHz, the period of the clock signal is known.
For 1 GHz (one cycle/second) the period is 1 ns (one nanosecond per cycle).
A real system clock provides an on signal for a portion of the clock period and an off signal for the remainder of the period.

## Slide 4: Gates based Flip Flops
Ideally we would like to allow for enough time for data to be written to registers and for stored data to propagate from registers to a CPU component such as the ALU.
To accomplish this, we need exact control of when the value stored in a register may be changed.
This could be accomplished using an impulse with a level triggered register, but providing an impulse based clock may limit some other features of the CPU.
Instead, we will develop an "edge-triggered" flip flop. That is, a flip flop whose value can only be changed on either the rising or falling edge of the clock.
To do so, we need more logic gates before our RS-Latch.

## Slide 5: Gates Based Flip Flops..
Essentially we need gates that provide an instant open and close for the data signal to enter when the clock rises or falls.
We won't go into the exact details of how this works. It is sufficient for you to understand that the signal for D is only recognized when the Edge Triggered Flip Flop sees either the rising edge of the clock or the falling edge.
This provides us with an exact time at which we know the data stored in a register can be changed.
We can use the rest of the time to allow the signal to travel to an adder or another component.
Examples of the component and gate based flip flops are provided on the examples page of the class website.

## Slide 6: Bit Shifting
Bit shifting is simply moving data stored in a register to the right or left and replacing the lost data.
In its most simple form, empty bit locations are replaced with either all one's or all zeroes.
Bits may be shifted to the left or right.
To perform a shift right logical (srl in assembly, and >> in C/Java) we will look at an example.
Assume we are given an 8 bit value: 01100101
Shifting to the right by one bit provides the following result: 00110010

## Slide 7: Bit Shifting..
We can control the number of bits by which we shift as well. We could shift a binary value to the left by 3 bit.
For example, shifting 10011001 to the left by 3 bits provides the following result: 11001000
A shift left logical is represented as "sll" in assembly and << in C/Java.

## Slide 8: Binary Multiplication
An example of binary multiplication is provided below.
1100 (12d)
*1011 (11d)
---------
1100
1100
0000
+1100
-----------
10000100 = 128d + 4d = 132d

## Slide 9: Binary Multiplication..
Notice that the result is computed by bit shifting the first multiplicand to the left based upon the location of each one in the second multiplicand and adding the result.
Additionally notice that shifting by one bit to the left effectively multiplies by two and shifting by one bit to the right effectively divides by two.
Next time we will look at finite state machines.
In a finite state machine (FSM):
  States are represented by circles;
  The ending state is represented by a circle within a circle; and
  Transitions between states are represented by arrows.