## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patterson and Hennessy Text

## Slide 2: Finite State Machines
Finite state machines - sequential logic function
  Consists of a set of inputs and outputs
  Contains a next state function that maps the current state and inputs to a new state Output
We will discuss synchronous state machines for JLS
  State changes are made with the clock cycle
  Only change is made on the clock edge
Let's investigate controlling a traffic light
See the class website for an example of the traffic light

## Slide 3: Moore Machine
Our output function will be restricted to depend upon the current state (this is a Moore machine)
  Notice that this means we would need a memory if we were to implement this using logic gates.
  The logic for a Moore state machine (including those in JLS) consists of both inputs and outputs
  Notice that we can form equations for a state machine, but it is easier to draw a diagram.
  In a state machine, circles (often with a name) are used to represent states.
  A circle contained within another circle represents a possible final or ending state.

## Slide 4: Contd..
Lines directed from one state to another with an arrow on one end of each line represent transitions from one state to another.
For a finite state machine, there must be deterministic transitions from one state to another. That is, a transition may not be ambiguous.
There exist other FSMs called Mealy machines wherein the output function can depend upon the current state and the input. We will not investigate Mealy machines.

## Slide 5: Traffic Signal Example
Consider a North-South / East-West set of traffic lights.
  Let's look at only the red and green lights.
  Let's also assume that there is a sensor that indicates there is a car at any of the given lights
  If the sensor for any of the given lights is true, it gives the vehicles in that direction the opportunity to move.
  We can assume that both E/W sensors are linked and both N/S sensors are linked such that only one of the pair needs to be active for both directions to be green at the same time.
  We will ignore turns for the purposes of our lights.
  We can then get by with two states. One for E/W and one for N/S. We need outputs for each state. Assume that a state's output is true if that state is active.

## Slide 6: Traffic Signal Example
A truth table follows:
E/W Sensor  N/S Sensor  E/W Out  N/S Out  Current State  Next State
---------------------------------------------------------------------------------------------------------- 0 0 1 0 0 0 0 0 0 1 1 1 1 0 1 0 0 0 0 1 0 1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 1 1 0 0 1 1 1 0 1 1 0
Notice that with a traffic light the current state must be retained as memory if
if this were to be implemented as a circuit.