## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patterson and Hennessy Text

## Slide 2: Single and Multi-Cycle CPUs
Recall that a CPU is made up of multiple components:
Program Counter and Instruction Register
  Program Counter - keeps track of the next instruction to load from instruction memory
  Instruction Register - stores the instruction to execute
These represent the fetch step.
Control Unit
  This portion of the CPU works to decode the instruction and guide the other portions of the CPU as to the current tasks to carry out It also ensures the fetch, decode, and execute cycle occurs in the proper order.

## Slide 3: Computer Components
Arithmetic Logic Unit (ALU), branching logic, and load/store logic
  This portion of the CPU works to execute the delegated instructions provided by the Control Unit
Registers - these store data on the CPU
Each CPU component plays an important role in the fetch-decode-execute cycle
Recall that both the program counter and portions of the execute cycle interact with memory
The Program Counter and the Instruction Register interact with instruction memory. Instruction memory is the portion of memory where instructions are stored.
During the execute step, the CPU may interact with data memory as well.

## Slide 4: Memory
An example of memory is provided on the class website in a JLS file.
Notice that memory is provided via a number of words of a particular size.
For example a memory may have a word size of 8 bits (1 byte) and there might be 64 words in memory.
That memory can then be addressed using 6 bytes since there are 2^6 = 64 possible values for a 6 byte unsigned binary value.
Memory is accessed by providing an address and providing inputs to specify whether a read or a write is occurs via the WE, CS, and OE inputs. A write occurs if WE and CS are both zero. A read occurs if CS and OE are both zero.
An example of a memory is provided on the examples page of the class website.

## Slide 5: CPU Cycle
Notice that there are multiple steps in the CPU cycle.
Provided we can transition from one step to the next and not need the data from the previous step after we have made the transition, it will be possible to have more than one instruction in the CPU at the same time
Fetch Decode Execute
        Fetch Decode Execute
                Fetch Decode Execute
Notice that if we have the situation above where instructions are fed to the CPU in a pipelined manner, we may have as many as three instructions in the CPU at once.
One could be in the fetch state, one in the execute and one in decode. In the next lecture, we will see how this is possible.